## Slide 1: JGCRP Meeting
25 September 2025
1
25/09/2025

## Slide 2: Agenda
25/09/2025
Introduction: 10 mins Welcome Members; Minutes and Actions from Previous Meeting. Modifications: 15 mins MPID339 and SPID_XX-2025 FASS Reserve Products Review Updates: 15 mins Fault-ride-through requirements for Demand Facilities; CRU; and Utility Regulator. AOB. 5 mins

## Slide 3: 1. Introduction: 10 minutes
  Welcome Members
  Minutes and Actions from Previous Meeting
25/09/2025

## Slide 4: MPID339 and SPID_XX_2025 FASS Reserve Products Review
25/09/2025
2. Modification: 10 minutes

## Slide 5: Background
In line with the TSOs commitments to deliver 2030 Renewable Energy Source (RES) targets and to align with the Clean Energy Package (CEP) and the Electricity Balancing Guideline (EBGL), the SEM Committee (SEMC) outlined in its High Level Design Decision on the System Services Future Arrangements, the need to:
  move to a day-ahead auction-based procurement of reserve system services; and
  to review the products to be procured in such an auction, and the development of a locational methodology that would support these objectives.
In Sept 2024, TSOs held a consultation on their Day Ahead System Services Auction (DASSA) Product Review and Locational Methodology, receiving 17 responses to the consultation.
Following a period of engagement with the Regulatory Authorities (RAs), the TSOs formally submitted their Recommendations Paper to SEMC, who then published their decision paper (SEM-24-074) published October 2024. SEMC’s decision was to approve the products recommended by the TSOs.
However, there are areas that SEMC requires the TSOs to give further consideration ahead of DASSA go-live. One of the areas is the interaction of the proposed services with the Grid Code, and this has driven both SONI and EirGrid to collaboratively develop Grid Code modification proposals directed at aspects of frequency control and reserve provision.

## Slide 6: Why was a Grid Codes Review needed?
The primary purpose of the Grid Codes is to preserve the integrity of the NI and IE transmission systems, enabling stable and secure operation of the systems and the safety of their users.
The Grid Codes accomplishes this by establishing:
Procedures for governing the actions of all transmission system users and the TSOs
Fundamental technical requirements for connecting to and operating on the transmission systems
Rules governing the operation, maintenance and development of the transmission systems

## Slide 7: Why was a Grid Codes Review needed?
Design and performance standards
Outage planning
Frequency control
Operating Margin
Information exchange
Operational testing
Emergency control and power system restoration
Monitoring, testing and investigation
Scheduling and dispatch
System Planning & Development
Definitions
And so the Grid Codes contain a range of requirements relevant to reserve system services:

## Slide 8: Main considerations for this Grid Codes review
Safe and secure operation of the system, and safety of its users
Long-term consumer value through volume limited procurement under FASS, and need for adaptability in the future arrangements
Development of a ‘System Services Code’
System services have traditionally been provided by synchronous generators, but increasingly by wind, demand side, battery storage units and other technologies
Partial alignment between DS3 arrangements and the Grid Codes
The introduction of 'downward’ reserve products that will mirror the existing ‘upward’ products across FFR, POR, SOR, TOR1, TOR2 and RR timeframes
EU Legislation (the Clean Energy Package and Electricity Balancing Guideline) require us to procure reserve services competitively and close to real-time.
User participation in the DASSA

## Slide 9: Purpose of this modification proposal
Not to place any additional mandatory technical Grid Code requirements on users that are not already present in the Grid Code, or present in custom and practice for reserve providers
Ensure that the Grid Code works cohesively and collaboratively with the System Services Market design (the DASSA for reserve system services) and the System Services Code, both currently under development, while also ensuring that Grid Code requirements related to frequency control and reserve provision are up to date and reflective of the changing system services landscape
Preserve fundamental requirements for frequency control and reserve provision in order to protect the safety and security of the Transmission System and its users.
  For example, the Grid Code will continue to require transmission system users to be compliant with all pre-existing Grid Code requirements related to frequency and reserve, and for relevant users, will still require operation at all times under the control of a governor control system/frequency response system which may only be restricted in specific circumstances as outlined in the Grid Code, e.g. where the action is essential for the safety of personnel.

## Slide 10
Proposed Changes:
Definitions

## Slide 11: New and modified reserve product definitions

## Slide 12: New and modified reserve product definitions contd.

## Slide 13: Inclusion of all relevant users, and upward and downward provision

## Slide 14: Frequency control modes

## Slide 15: Outage planning

## Slide 16: System Services Code

## Slide 17
Proposed Changes:
System Planning & Development

## Slide 18: Housekeeping

## Slide 19
Proposed Changes:
Design and performance standards

## Slide 20: Existing requirements for reserve capability

## Slide 21: User-specific terminology

## Slide 22
Proposed Changes:
Outage Planning

## Slide 23: Inclusion of all relevant users

## Slide 24: Inclusion of all relevant users

## Slide 25
Proposed Changes:
Frequency Control

## Slide 26: System Services for Frequency control

## Slide 27: Frequency control modes

## Slide 28: Inclusion of all relevant users

## Slide 29
Proposed Changes:
Operating Margin

## Slide 30: Upward and downward provision of reserve

## Slide 31: Consolidating clauses/removal of repetition

## Slide 32: Significant Frequency deviations, i.e. ‘Frequency Events’

## Slide 33: Contingency Reserve

## Slide 34
Proposed Changes:
Information Exchange

## Slide 35: Inclusions of all relevant users

## Slide 36
Proposed Changes:
Operational Testing

## Slide 37: Inclusions of all relevant users

## Slide 38
Proposed Changes:
Emergency Control and Power System Restoration

## Slide 39: Inclusions of all relevant users

## Slide 40
Proposed Changes:
Monitoring, Testing & Investigation

## Slide 41: Inclusion of all relevant users/user specific terminology

## Slide 42
Proposed Changes:
Scheduling & Dispatch

## Slide 43: Interactions with other Codes

## Slide 44: Consolidating clauses/removal of repetition

## Slide 45: Inclusion of all relevant users

## Slide 46: Interactions with other Codes

## Slide 47: Inclusion of all relevant users

## Slide 48: Recap: Purpose of this modification proposal
Not to place any additional mandatory technical Grid Code requirements on users that are not already present in the Grid Code, or present in custom and practice for reserve providers
Ensure that the Grid Code works cohesively and collaboratively with the System Services Market design (the DASSA for reserve system services) and the System Services Code, both currently under development, while also ensuring that Grid Code requirements related to frequency control and reserve provision are up to date and reflective of the changing system services landscape
Preserve fundamental requirements for frequency control and reserve provision in order to protect the safety and security of the Transmission System and its users.
  For example, the Grid Code will continue to require transmission system users to be compliant with all pre-existing Grid Code requirements related to frequency and reserve, and for relevant users, will still require operation at all times under the control of a governor control system/frequency response system which may only be restricted in specific circumstances as outlined in the Grid Code, e.g. where the action is essential for the safety of personnel.

## Slide 49
Thank you!
Questions?
25/09/2025

## Slide 50: 4. Updates: 10 minutes
  Fault-ride through requirements for Demand Facilities;
  CRU; and
  Utility Regulator.
25/09/2025

## Slide 51: Proposed Fault Ride-Through Requirements for Demand Facilities
September 2025 JGCRP Meeting
25/09/2025

## Slide 52: Data Centre Fault Response – Actual Events
A number of significant data centre demand reduction events have been observed on the power system.
The level of fault-initiated reduction in data centre demand has increased as data centre demand increases.
Disturbance propagation (contour map) and collective Data Centre Response (08 May 2025, 220 kV fault in Dublin)
Retained Voltage [%]
Chart: Time [S]
Date | Transmission System Contingency | Data Centre Demand Reduction | Percentage of Total Data Centre Demand
7 Jan 2022 | Limerick: Killonan-Kilpaddoge 220 kV Fault | 74 MW | 16%
13 Dec 2022 | Dublin: Kellystown-Woodland 220 kV Fault | 204 MW | 34%
26 Jan 2025 | Dublin: Poolbeg 220 kV Reactor Fault | 321 MW | 44%
8 May 2025 | Dublin: North Wall – Poolbeg 220 kV Fault | 387 MW | 52%

## Slide 53: Information Paper for Stakeholder Review
Contents
Executive Summary
Background
Examples of Observed Response
Power System Analysis
Addressing the Issue
Proposed Grid Code Requirements
Next Steps
Appendices

## Slide 54: Existing and Proposed New Grid Code Requirements
Requirement | Non DCC | DCC
Requirements for different Voltage ranges​ | NEW: Remain synchronised to the Transmission System and operate within the ranges of the Transmission System Voltage at the connection point, for an unlimited time period, as specified below:​ 400 kV system: 360 kV to 420 kV (0.9 p.u. – 1.05 p.u.)​ 220 kV system: 198 kV to 245 kV (0.9 p.u. – 1.114 p.u.)​ 110 kV system: 99 kV to 123 kV (0.9 p.u. – 1.118 p.u.)​ | EXISTING: Remain synchronised to the Transmission System and operate within the ranges of the Transmission System Voltage at the connection point, for an unlimited time period, as specified below:​ 400 kV system: 360 kV to 420 kV (0.9 p.u. – 1.05 p.u.)​ 220 kV system: 198 kV to 245 kV (0.9 p.u. – 1.114 p.u.)​ 110 kV system: 99 kV to 123 kV (0.9 p.u. – 1.118 p.u.)​
Requirements for Frequency range and operational time Frequency | NEW: Minimum Time Periods for Demand Facilities, Closed Distribution Systems and Distribution Systems to Remain Operational without Disconnecting​ Frequency Range Time Period​ 47 – 47.5 Hz 20 seconds​ 47.5 – 48.5 Hz 90 minutes​ 48.5 – 49 Hz 90 minutes​ 49 – 51 Hz Unlimited​ 51 – 51.5 Hz 90 minutes​ 51.5 – 52 Hz 60 minutes​ | EXISTING: Minimum Time Periods for Demand Facilities, Closed Distribution Systems and Distribution Systems to Remain Operational without Disconnecting​ Frequency Range Time Period​ 47 – 47.5 Hz 20 seconds​ 47.5 – 48.5 Hz 90 minutes​ 48.5 – 49 Hz 90 minutes​ 49 – 51 Hz Unlimited​ 51 – 51.5 Hz 90 minutes​ 51.5 – 52 Hz 60 minutes​
ROCOF requirement | NEW: Remain connected to the Transmission System during rate of change of Transmission System Frequency of values up to and including 1Hz per second as measured over a rolling 500 milli-second period. (Voltage dips may cause localised RoCoF values in excess of 1 Hz per second for short periods, and in these cases, the Fault-Ride Through clause (Reference TBC) supersedes this clause (Reference TBC) | 
FRT requirement | NEW: Demand Facilities shall remain connected to the Transmission System during and following any Fault Disturbance on the Power System which results in a Voltage deviation which remains on or above the voltage-against-time profile specified in (EirGrid/SONI Grid Code Reference TBC) at the Connection Point. | 
Active Power Recovery Requrement | NEW: Following clearance of the Fault Disturbance, the Demand Facility should return to at least 95% of its pre-fault Demand within 500 milliseconds of the Transmission System Voltage recovering to 90% of the nominal Voltage. The post Fault Disturbance ramp up rate for the Demand Facility, shall be coordinated and agreed between the TSO and the Demand Facility owner. | 

## Slide 55: Proposed Grid Code Requirements
Chart: Time (seconds)
| 0 | 0 | 0.15 | 0.15 | 0.45 | 0.45 | 2
 | 0 | 0 | 0 | 0.5 | 0.5 | 0.9 | 0.9
Required Voltage against time profile as proposed as part of forthcoming EirGrid/SONI code modification proposal
Demand Facilities shall remain connected to the Transmission System during and following any Fault Disturbance on the Power System which results in a Voltage deviation which remains on or above the voltage-against-time profile specified in (EirGrid/SONI Grid Code Reference Figure TBC) at the Connection Point.
Following clearance of the Fault Disturbance, the Demand Facility should return to at least 95% of its pre-fault Demand within 500 milliseconds of the Transmission System Voltage recovering to 90% of the nominal Voltage. The post Fault Disturbance ramp up rate for the Demand Facility, shall be coordinated and agreed between the TSO and the Demand Facility owner.

## Slide 56: Next Steps
Progress the Fault Ride-Through Grid Code modification proposals supported by publication of an industry information paper and hosting of an industry webinar.
  Publication of industry information paper, September 2025
  Feedback on the Grid Code proposals (and the information paper) may be provided to: EirGrid Grid Code team: GridCode@eirgrid.com
  SONI Grid Code team: GridCode@soni.ltd.uk
  EirGrid and SONI hosted industry webinar, stakeholder participation invited, October 2025
  Bring the proposed modification to the Grid Code Panel for support, December 2025

## Slide 57: JGCRP/ GCRP Meeting 26 June 2025
CRU Update
JGCRP Modifications Update since 26 June 2025
New Modification requests: 1 (MPID 319)
Joint Modification recommendations under review: 3 (MPID 293, MPID 319, MPID 327)
www.cru.ie

## Slide 58: AOB
Meeting Minutes will be issued by COB 09 October 2025
58
25/09/2025